## Slide 1: Council’s GHG emissions
Interim results from 23/24FY greenhouse gas (GHG) inventory audit

## Slide 2: Key results
For the 23/24FY Councils emissions were 3,489tCO2-e (excluding staff commuting).
This is a reduction of -11.3% (-446tCO2-e) compared to the 22/23FY.
The reduction is primarily due to improvements to wastewater processing and sustained lower emissions from electricity.
The latest GHG inventory report included two new sources of emissions:
  43tCO2-e produced by wood pellet cartage, and
  371tCO2-e from staff commuting.*

## Slide 3: Emissions by BU
Chart: Total emissions (tCO2e) by business unit
| Water and Wastewater Treatment | Aquatic Facilities | Operations | Leisure and Open Space | General Council | Property | Access and Transport
2023/2024 | 2180.8968 | 667.2397 | 270.2023 | 113.9677 | 100.8317 | 90.7023 | 67.0208

## Slide 4: Emissions reductions/ increases
Total gross emissions reduced by 11.3%
Source | % | tCO2-e
Refrigerant | -80% | -149
Sludge to landfill | -60% | -231
Air travel | -43% | -8
Wastewater processing | -16.7% | -271
Petrol | -3.7% | -3
Source | % | tCO2-e
Fertiliser | +188% | +8
Electricity | +23% | +144
Natural gas | +10% | +41
Diesel | +2% | +10
Wood pellet freight (NEW) |  | +43

## Slide 5: Targets
Target | 23/4FY Performance
Reduce emissions by 80% compared to 2009/10, by 2022 | 82.8% (excluding wastewater) 72% (including wastewater)
Further reduce Category 1 and 2 emissions by 15.5% (compared to 2022) by 2032 | 24.7%* Council officers will work with Toitū to determine whether we must update this target.
*This is highly dependent on emissions reductions from wastewater treatment and electricity compared to the 2022 baseline.

## Slide 6: Progress against target
Chart: Category 1-6 emissions reduction against 2009/10 baseline
| 2010/11 | 2011/12 | 2012/13 | 2013/14 | 2014/15 | 2015/16 | 2016/17 | 2017/18 | 2018/19 | 2019/20 | 2020/21 | 2021/22 | 2022/23 | 2023/24
% change (excl ww) | 0.113 | 0.258 | 0.471 | 0.484 | 0.431 | 0.566 | 0.751 | 0.759 | 0.77 | 0.778 | 0.752 | 0.771 | 0.81518 | 0.82848
Target for 2021/22 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
% reduction (incl ww) | 0.05814 | 0.086848 | 0.30088 | 0.31347 | 0.26022 | 0.39647 | 0.5814 | 0.58901 | 0.60085 | 0.60883 | 0.62024 | 0.64062 | 0.68425 | 0.72007

## Slide 7: Progress over time
Chart: CO2 equivalent emissions (tonnes) and percentage reduction in emissions from baseline year
| 2009/10 | 2010/11 | 2011/12 | 2012/13 | 2013/14 | 2014/15 | 2015/16 | 2016/17 | 2017/18 | 2018/19 | 2019/20 | 2020/21 | 2021/22 | 2022/23 | 2023/24
Gross emissions (incl WW) | 14578 | 13195 | 11387 | 8718 | 8561 | 9225 | 7526 | 5220 | 5125 | 4977.4 | 4877.95 | 4735.6626 | 4481.5 | 3937.3804 | 3490.7117
Percentage reduction against 2009/10 baseline | 0.05814 | -0.086848 | -0.30088 | -0.31347 | -0.26022 | -0.39647 | -0.5814 | -0.58901 | -0.60085 | -0.60883 | -0.62024 | -0.64062 | -0.68425 | -0.72007

## Slide 8: Update on Category 3-6 emissions
Staff commuting and wood pellet freight are new sources of Category 3-6 emissions.
Based on value, Council’s supplier based emissions for 23/24FY are 11,851tCO2-e which is more than double the 22/23FY.
Expanding monitoring and reporting of these emissions is a key work programme for the Climate Action team.

## Slide 9: Improving how we use energy
A cross-Council group has been working with an energy specialist to identify opportunities to improve energy efficiency.
For example, there is an opportunity to reduce electricity consumption by ~18% saving $10,000 in electricity used by the Civic Building.
We are exploring other opportunities across Council assets and services.

## Slide 10: Next steps
We will notify you if the interim results are different to the final verified results.
We will continue to work with asset managers to pursue opportunities to reduce emissions.
We will continue to develop targets for category 3 to 6 emissions for introduction by the end of 2025.